## Slide 1
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
Yoseftal Medical Center, Eilat
Example Proposal 1
AdvantCare nurse call system
1 ward section · 8 rooms × 3 beds · 8 en-suite bathrooms · 1 nurse station
Orad – Advantecnia distributor in Israel · 26/10/2026
Notes: IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.

## Slide 2
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
SCOPE
What the example includes
1
ward section(s)
8
rooms (3 beds each)
24
beds
8
en-suite bathrooms (toilet + shower + basin)
1
nurse station(s)
1
server (LVNS)
Each bed: red call panel with bayonet socket + pear handset 2 m.
Each room: green presence / cancel button inside by the door, 3-colour corridor light above the door.
Each bathroom: SOS pull-cord beside the toilet and beside the shower, presence / cancel button outside and a light above the door.
Room controllers (PCB ECV169) in the corridor ceiling, daisy-chained on one bus per section to the SmartHub in the section rack.
Nurse station outside the rooms with an iPad (Consola Monitor): every call, presence, history and statistics.
LVNS server + switch + UPS + rack – everything needed for the system to work.

## Slide 3
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
PLANS
Floor plan · ward section A

## Slide 4
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
PLANS
Typical room + en-suite bathroom

## Slide 5
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
PLANS
System architecture

## Slide 6
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
EQUIPMENT
Advantecnia devices and system components
24 ×
Bed call panel, red, with bayonet socket for pear handset
ACE82012153 · 3 per room × 8 rooms
24 ×
Pear handset, 1 capacitive button, 2 m cable, bayonet
ACE39060521 · 1 per bed × 24 beds
16 ×
Presence / cancel panel, green
ACE82082137 · 8 rooms (by the door) + 8 bathrooms (outside)
16 ×
SOS mechanism with pull-cord (toilet / shower)
ACE40320303 · 2 per bathroom (toilet + shower) × 8
16 ×
Corridor light, 3 colours (red · green · blue)
EOP004 · 8 rooms + 8 bathrooms (above the door)
24 ×
Room controller PCB 24 pins, 12–48 V DC
ECV169 · 2 per room + 1 per bathroom = 24
1 ×
SmartHub connectia – head of the controller bus
EVV049 · 1 per ward section
1 ×
LVNS server – local server & notifications
EOP006 · 1 server for the whole system
1 ×
Nurse station iPad 10.9" Wi-Fi 128 GB
EOP002 · 1 per nurse station
1 ×
ionTab client/server licences + MDM (1st year included)
EVV038 · 1 per ward section
1 ×
PoE switch 24 ports, managed
ACESWP24P · 1 per ward section rack
1 ×
Wall rack 19" 9U with PDU, shelf and cable management
RACK9U · 1 per ward section
1 ×
UPS 1500 VA online, rack mount
UPS1500 · 1 per rack
1 ×
Wi-Fi 6 access point, PoE, at the nurse station
WAP6 · 1 per nurse station

## Slide 7
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
NURSE STATION
Every call in one place – outside the rooms
Consola Monitor on the nurse iPad: room, bed and type of every call
Red = call · green = nurse in the room · blue = code blue
Presence / cancel by the door closes the call
History and statistics: waiting and response times
One nurse station for the section

## Slide 8
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
INTERACTIVE PLAN
3D model, walk-through and live simulation
3D model of the ward: equipment and wiring
Walk-through with realistic photos
Live simulation: call, presence, code blue
Consola Monitor at the nurse station
Documents: proposal, scheme, plans, BOQ
Scan to open
alexjusid-jpg.github.io/planos/yoseftal_ex1/en/

## Slide 9
IMPORTANT – THIS IS NOT A REAL, FORMAL OR OFFICIAL PROPOSAL. It is an example only, prepared to support the offer that Orad must make to the end client.
NEXT STEPS
From this example to a real proposal
01
Consultation form
Orad fills in the form with the real data of the ward
02
Site plans
Real floor plans, ceiling and cable routes
03
Technical proposal
ACE BG confirms codes, quantities and prices
04
Orad offer
Orad prepares the official offer for the hospital
Yoseftal Medical Center, Eilat · ORAD-YOS-EX1-2026-10 · 26/10/2026